## Slide 1: Flexible ASIC-based OpenFlow pipeline
Shaun Wackerly, HPE Aruba <wackerly@hpe.com>

## Slide 2: Overview
Flexible ASIC tables
Tools
ovs2json
pipeline constructor
How it’s done in FAUCET

## Slide 3: Flexible ASIC tables
HPE Aruba 6th generation ASIC
  5400Rv3
  3810
  2930
Table types
  TCAM, wildcardable (up to 8K entries)
  Hash, exact-match (up to 64K entries)
Reconfigure pipeline at run-time
  No reboot, OF disable, firmware change, or licensing needed

## Slide 4: Tool: ovs2json
Read flows from OVS
  extract match fields & entry counts
  produce JSON pipeline definition
Use case
  have existing application or solution implemented virtually (OVS)
  want to deploy on HPE Aruba switches for scale/performance

## Slide 5: Tool: Pipeline constructor
Construct pipeline via GUI
  table size
  table ordering
  match fields/type
  All actions are automatically included
Use case
  have idea for application
  want to speculate if implemented (at scale) on an HPE Aruba switch

## Slide 6: How it’s done in FAUCET
OFPMP_TABLE_FEATURES request**
  Empty body: Read pipeline
  Full body: Define pipeline
In the code:
  faucet/valve.py – Identifies switch type, verifies pipeline
  faucet/tfm_pipeline.py - Parse JSON & define pipeline
    Parse JSON file (LoadRyuTables.load_tables)
    Send to switch (valve_of.table_features)
** OpenFlow 1.3.5 spec, section 7.3.5.5

## Slide 7: Thank you
Shaun Wackerly, HPE Aruba <wackerly@hpe.com>